## Slide 1: New Frontiers in CT Data Quantification
Now (or coming soon) in Blob3D
Automated shape classification
Apollo 17 cores and lunar sedimentology
Rich Ketcham
UTCT
Jackson School of Geosciences
University of Texas at Austin

## Slide 2: How to separate?

## Slide 3: The Watershed Algorithm
Main Idea:
Identify “watersheds” separated by “divides”
Usual method: Basin Fill
  Mark low points/basin centers
Credit: ImageJ Wiki
Example CT number traverse

## Slide 4: The Watershed Algorithm
Main Idea:
Identify “watersheds” separated by “divides”
Usual metehod: Basin Fill
  Mark low points/basin centers
  Start adding water from bottom, at markers
    How: Maintain a list of all points adjacent to marked areas, sorted by elevation
    Claim them one by one, in elevation order, according to their marker
    Add new adjacent points to list
  When two areas merge, mark their boundary
Credit: ImageJ Wiki

## Slide 5: Rainfall Watershed
One-pass watershed (fast!)
  Rainfall method (based on Bieniek & Moga 2000)
    Follow each drop downhill
    Classify all voxels in path
    Stop when hit classified voxel
  Faster than any current open-source watershed algorithm

## Slide 6: What defines “topography”?
Distance transforms:
Brightness = distance from nearest edge
EDT: Euclidean Distance Transform
SADT: Smoothed Approximate Distance Transform
CT data
Ketcham, 2025

## Slide 7: Marking high (or low) points
Ketcham, 2025

## Slide 8: Interactive watershed processing
Segmented subvolume; red lines indicate cut faces with more data beyond
Watershed applied
Blobs on cut faces postponed for later processing;
rest are accepted or refined further
Time required reduced to a few seconds/grain

## Slide 9: Post-watershed smoothing
No smooth
Smooth = 1
Smooth = 2

## Slide 10: Application: detrital zircon
Epoxy grain mounts
  4-6 mm diameter
  100’s-1000’s of zircon grains
Want to measure
  Size
  Shape
  Crystal morphology
Match to laser U/Pb date
  Need to get every grain right!

## Slide 11: Shape analysis behind the scenes

## Slide 12: Extracting crystal shapes
“Box”
“Shape”
C: Shortest axis
B: Shortest ortho to C
A: Axis ortho to B+C
A: Longest axis
B: Longest ortho to A
C: Axis ortho to A+B
From Blott and Pye, 2008
Stereonet

## Slide 13: Reading crystal face nets
prism face 1
prism face 1
prism face 2
prism
face 2
py
py
py
py
py
90°
45°
Each isosurface facet orientation (normal) projected to stereonet

## Slide 14: Reading crystal face nets
Preliminary statistics:
high correlation coefficient = symmetry = crystallinity
high standard deviation = angular
Well-formed crystal (corr. = 0.74, skew = 4.9)

## Slide 15
Crystalline but slightly rounded
Crystal shard; some fair faces, one paired set.
Crystal shard; possibly rounded remnants.

## Slide 16: Reading facial angles
Ideal zircon 100-101: 47.85
0
1
2
3
4
5
Strength
Interfacial Angles
0
1
5
3
4

## Slide 17: What crystal form might tell us
after Pupin (1980)

## Slide 18: Reading facial angles
Pyrrhotite (from Ryugu)

## Slide 19: Grain classification (by human)
Each grain assigned code by human:
  A,B,C,D: Geometry
  1,2: Roughness
  Codes for tips
  1-4: Confidence
Using both 2D and 3D data
Over 5000 grains classified in 4 samples
from O’Leary MS Thesis (2025),
after Zeigler et al. (2023)

## Slide 20: Autoclassification with Random Trees ML
Using Weka (Waikato Environment for Knowledge Analysis) v3.8.6
5.34 ( 2565) XlStdev(mh)
4.68 ( 2256) XlRdev
2.96 ( 1292) Shape Factor(D05)
2.59 ( 1535) c/b
2.35 ( 1593) Sphericity
1.86 ( 2859) XlCorr(mh)
A
B
C
D
Grain Shape

## Slide 21: Autoclassification with Random Trees ML
Using Weka (Waikato Environment for Knowledge Analysis) v3.8.6
1.11 ( 1439) Sphericity
0.92 ( 4588) SNSVR
0.68 ( 5052) XlStdev(mh)
Unbroken
Broken
Brokenness

## Slide 22
End of Part 1

## Slide 23: Sedimentological Analysis of In Situ Lunar Regolith from Apollo 17 Double Drive Tube 73001/2 using X-ray Computed Tomography
Melanie Garza
Master’s Thesis

## Slide 24: Sample Collection
73002: 430 g and 20 cm (upper section)
73001: 803 g and 35 cm (lower section)

## Slide 25
73002 (2019)
73001 (2021)

## Slide 26
Soil clod
“Ped”
Disrupted Regolith
Impact Melt Breccias
Regolith Breccias
High-Ti Basalts
73002
73001
Scan Data

## Slide 27: Objectives
XCT images allowed to observe regolith from a lunar landslide, providing an opportunity to gain insight into sedimentary processes on the surface of the moon.
  How did spillage affect scan data interpretation?
  How does lunar regolith density vary with depth?
  How does particle distribution and shape vary with lithology?
  What processes do particles undergo on the lunar surface to create varying degrees of rounding?

## Slide 28: Disruption in 73002
Also: 1973 X-ray

## Slide 29: Ped Curvature
Lunar soil peds in 73002 exhibited flat/curved surfaces.
Curvature tests showed ped surfaces measured at or below the 4.12 cm tube diameter. Thus, they were created during collection.
Peds reflect the true state of the regolith prior to disruption.

## Slide 30: Verifying post-correction CT numbers
Used histograms of high-Ti basalts (prominent phases: plagioclase, pyroxene, ilmenite), air, Al tube

## Slide 31: Lunar Soil Density & CT Numbers
A central volume of interest (VOI) was placed within peds in 73002 and in areas of regolith in 73001 to develop a profile.
Histogram mode is representative of lunar dust compaction.

## Slide 32: Regolith Density Down the Core
77 peds were sampled in 73002
21 VOIs were sampled in 73001.
Regolith density decreases with depth down the core.
Unexpected!
LOST FROM SPILLAGE

## Slide 33: Deep Learning Segmentation
How can shape data be acquired?
Sensor3D and U-Net models were trained to classify high-Ti basalts, regolith breccias, and impact melt breccias.
3D shape data created across the core through segmentation.

## Slide 34: Deep Learning Segmentation
Many challenges . . .
Multiple days spent training models
High-Ti basalts segmented a smaller clasts size that was not possible for regolith and impact melt breccias.
Grayscale and textural similarities required deep learning to differentiate clasts.

## Slide 35: High-Ti Basalts
After Blob3D processing, 793 high-Ti basalts were segmented. 231 (73002) and 562 (73001)
Majority of clasts are small. Larger clasts are found clustered in 73002 and distributed in 73001.
Last ~30% of 73001 has an absence of large clasts.

## Slide 36: Regolith & Impact Melt Breccias
Regolith breccias (blue) include 91 clasts. 56 (73002) and 35 (73001)
Impact melt breccias (yellow) include 100 clasts. 44 (73002) and 56 (73001)
Reminder: Smaller clasts present, but not segmented.
There is an apparent fining downward. Last ~20% of 73001 also has no large breccia clasts.

## Slide 37: Rounding from the Landslide
Short / Intermediate Axis
Intermediate / Long Axis

## Slide 38: Rounding and Fragmentation on the Lunar Surface
Universal Fragmentation Law
High-Ti Basalts
Short / Long Axis
Intermediate / Long Axis
Regolith Breccias
Impact Melt Breccias
Long Axis (mm)
Fragmentation line

## Slide 39: Conclusions/Interpretations
Peds aided in reconstructing the soil density despite the disruption. Density decreased with depth in the core  Unexpected!
3D models of lithologies were created using machine learning segmentation.
Regolith and impact melt breccias show more rounding than high-Ti basalts. High-Ti basalts show signals of rounding in the smallest particle size not available in the other two lithologies.
Rounded particles could be a result of the 10 km distance, including 5 km runout, traveled during the Light Mantle landslide.

## Slide 40
End of Part 2

## Slide 41: The Carbonado Conundrum
Polycrystalline
  Bimodal: 10’s -100’s µm and ~1 µm
Found only in Brazil and Central African Republic
Age 2.6-3.8 Ga
Large (up to 3167 carats)
Light d13C: -24 to -26 ‰
Highly porous, nm to mm scale
Patinaed surfaces
Crustal inclusion suite
  florencite (hydrous REE phosphate)
  native metal: Fe, Ni-Pt, SiC, etc.
  No mantle minerals

## Slide 42: 3D Petrographic Microscope

## Slide 43: Old-fashioned petrography…in 3D!
5 mm
Observations with 29-µm resolution data
  Large bright grains only near rim (zircon stuck in pore)
  Megapores only near rim
  Banding beneath patinaed surface
  Grading of small inclusions

## Slide 44: Interpreting CT numbers
Chart: Attenuation (μ) vs. Source Energy
| 10 | 15 | 20 | 30 | 40 | 40.44 | 40.450000000000003 | 50 | 60 | 80 | 100 | 150 | 200 | 300 | 400 | 500
florencite | 245.23 | 82.698 | 37.948 | 12.9238 | 6.1934 | 6.0144 | 26.8142 | 15.6446 | 9.845 | 4.7972 | 2.821 | 1.2136 | 0.76254 | 0.47972 | 0.38306 | 0.33008
diamond | 8.3317 | 2.837 | 1.5539 | 0.89997 | 0.73122 | 0.6574 | 0.61521 | 0.566 | 0.53084 | 0.47459 | 0.43241 | 0.37616 | 0.33573 | 0.30655
pyrope | 61.7179 | 18.8019 | 8.2565 | 2.8638 | 1.5546 | 1.0818 | 0.86505 | 0.67628 | 0.59318 | 0.49682 | 0.44596 | 0.38256 | 0.34115 | 0.31092
kaolinite | 42.849 | 13.0663 | 5.7661 | 2.0234 | 1.1135 | 0.78556 | 0.63216 | 0.4999 | 0.44172 | 0.3703 | 0.33327 | 0.28566 | 0.25551 | 0.23302
almandine | 294.9194 | 97.155 | 43.6118 | 14.0767 | 6.477 | 3.6919 | 2.4354 | 1.4033 | 1.0147 | 0.68224 | 0.56998 | 0.46634 | 0.40978 | 0.37135

## Slide 45
140 kV, μeff > almandine
40 kV, μeff ≥ almandine
40 kV, μeff ≥ apatite
40 kV, μeff ≥ calcite

## Slide 47: 3D shape analysis (SVD)
Shows preferred orientation; oblique to grading and patinaed surface

## Slide 48: 5-µm resolution data (5 mm FOV)

## Slide 49: 5-µm observations
Fabric mainly in small inclusions
Mid-sized pores parallel inclusions
Virtually all inclusions polymineralic
Disequilibrium textures
Dodecahedral pseudomorphs

## Slide 50: Dual-energy scanning
60 kV
120 kV

## Slide 51
1-µm resolution data (1 mm FOV)

## Slide 52: Setting up the cut

## Slide 53: D’oh!

## Slide 54: SEM and EDS
Extensive but heterogeneous microporosity
Most common minerals kaolinite and florencite

## Slide 55: A rough model
Micro-diamonds, other phases settle in magma chamber(?)
Remnant liquid rich in C, incompatibles (U, REE)
Bubbles are trapped, but tend to rise
Sudden shear event deforms bubbles
Pressure change massively increases diamond nucleation rate
<1 µm diamonds nucleate, deform while growing

## Slide 56: A rough model
Over time (Gyrs), radiation damage destroys dodecahedral phase
Atoms migrate through pore network, recrystallizing at shallow P,T
“AWOLite”?

## Slide 57: But you can’t do just one!
New images by Scott Eckley
5 mm
Inclusion long and short axes
Another pseudomorph?
Spatially vary pore filling - original mineralogy, limited migration?

## Slide 58: 3D Imaging
tarynstravelswithkayla.blogspot.com

## Slide 59: Fractured limestone
Voxel size: 0.042 mm(!)
Specimen courtesy of Dr. Brenda Kirkland-George; Scanned summer 1997

## Slide 60: The same, in reverse
Homo sapiens calcaneus
trabeculae
1 cm
Felis concolor skull
turbinates
1 cm

## Slide 61: Thin features look dimmer… why?

## Slide 62: What’s behind the blurring?
Each pixel = 86 µm
1) Partial Volume Effect
2) Other blurring from…
Large X-ray focal spot
Large detectors
Detector crosstalk
CT reconstruction algorithm
Scanner acting up that day…
Geometric imprecision
System noise

## Slide 63: Point-Spread Function (PSF)
*

## Slide 64: PSF and Thin Features
“Real”
thickness
Measured
profile
1-2D Example: Membrane thickness

## Slide 65: Fracture Shades of Gray
Pixel size = 50 µm

## Slide 66: So what?
Thresholding can remove the effects of blurring when the feature is large compared to the PSF.

## Slide 67: Stepping back
Correct threshold for thick bone: 144
Lower threshold half way to air: 84
Lower by half again: 54
And half again…: 39
Down to: 30

## Slide 68: Same with trabeculae
Not enough!
Too much!

## Slide 69: Rule 6 for picking the correct CT number for segmenting thin features
There is no correct CT number for segmenting thin features

## Slide 70: What resolution do we “need”?
5 mm
30 mm
80 µm resolution
22 µm resolution

## Slide 71: Histogram methods dangerous!
“Hi-res”
Otsu/Trussell = 110
Vol frac = 0.20
“Lo-res”
Otsu/Trussell = 94
Vol frac = 0.28
Smoothing shifts lower-abundance phase as f(surface area)

## Slide 72: The upshot…
If features are small with respect to the PSF, thresholding cannot give a correct result
  Including adaptive thresholding, indicator kriging, iterative optimization, etc.
  If the method is based on histogram analysis, that’s a bad sign
What to do:
  Get better data (if you can)
  Interpret your data with modesty
  Measure the PSF and use it

## Slide 73: Counting up the attenuation

## Slide 74: Deconvolution made simple
*
=
Reality
(albeit pixelated)
Inconvenient
reality
(or reasonable representation thereof)
What we get
Take this…
… someplace where we can assume this…
… and figure this out

## Slide 75: Using the PSF to measure aperture
Model (fitted) PSF Noise Data

## Slide 76
Blob3D
PSF Measurement Tool
Calculates a raw PSF and a mean PSF based on 9 parallel traverses
Corrects for non-orthogonality of the intersection plane, voxel anisotropy
Accumulate a list of PSFs over a dataset
Also measures orientation of interface
PSF param = 4s
(diameter of region with 95% of signal from voxel)

## Slide 77: Solution: Measure and use PSF
Required “knowledge”: PSF parameters, air CT number

## Slide 78: IPSF in action
New Blob3D tool

## Slide 79: IPSF vs. Thresholding
Subtle density contrast
Severe density contrast
Key point: the more information you provide, the better you can do
Threshold
Threshold

## Slide 80
End of Part 2

## Slide 81: Moving on to 3D…
Au grains in quartz and chalcopyrite, Grasberg mine, Irian Jaya (from Kyle and Ketcham 2003)
GOLD!!!
Issues:
High atomic number; artifacts
Odd shapes
Economic at ppm (or g/t) level; scan a lot to see a little
  Particles usually “small” with respect to scan resolution

## Slide 82: A simple experiment
1 mm
Gold grains
(with a little silver mixed in)
2D images; scale bars all 200 µm
This and following from Ketcham and Mote (2019), JGR

## Slide 83: A simple experiment (c. 2004)
10 mm
“Core” placed in series of
cylinders with more quartz powder
Grains embedded in quartz+epoxy “sandstone core”
The Question: Can we get the same answer when measuring across grain sizes and scan resolutions?

## Slide 84: A hint of problems ahead
Scan/recon parameters unchanged except FOV
Grains both blurrier and darker at low resolution
  Blurring/partial volume effects
  Beam hardening
10 mm FOV
50 mm FOV

## Slide 85: A simple experiment (updated 2018)
10 mm
“Core” placed in series of cylinders with more quartz or garnet powder
The Question: Can we get the same answer when measuring across grain sizes, scanners, enclosing materials, and scan resolutions?
ACTIS
MicroXCT

## Slide 86: How to segment and measure?
Threshold segmentation: what value to use?
10-mm ACTIS scan (10 µm resolution)
  Matrix ~40, Au-max ~160
  Threshold at 100?
Chart: 10 mm FOV
| 1.9518140589569164E-2 | 1.8990929705215421E-2 | 1.060657596371882E-2 | 6.422902494331066E-3 | 4.4841269841269845E-3 | 7.8854875283446701E-3 | 2.1882086167800455E-3 | 2.5340136054421768E-3 | 2.8571428571428567E-3 | 4.2687074829931967E-3 | 4.4501133786848069E-3 | 7.0861678004535147E-4
Thresh 100 | -0.41165 | -0.23638 | -0.25151 | -0.14718 | -0.39561 | -0.24561 | -0.22026 | -0.2867 | -0.47525 | -0.32746 | -0.22427 | -0.49979

## Slide 87: How to segment and measure?
Threshold segmentation: what value to use?
10-mm ACTIS scan (10 µm resolution)
  Matrix ~40, Au-max ~160
  Threshold at 100?
Chart: 10 mm FOV
| 1.9518140589569164E-2 | 1.8990929705215421E-2 | 1.060657596371882E-2 | 6.422902494331066E-3 | 4.4841269841269845E-3 | 7.8854875283446701E-3 | 2.1882086167800455E-3 | 2.5340136054421768E-3 | 2.8571428571428567E-3 | 4.2687074829931967E-3 | 4.4501133786848069E-3 | 7.0861678004535147E-4
Thresh 100 | -0.41165 | -0.23638 | -0.25151 | -0.14718 | -0.39561 | -0.24561 | -0.22026 | -0.2867 | -0.47525 | -0.32746 | -0.22427 | -0.49979
Thresh 90 | -0.062088 | 0.033156 | -0.039162 | 0.10921 | -0.15061 | 0.00063819 | 0.077553 | -0.069496 | -0.18398 | -0.04431 | 0.014687 | -0.22328

## Slide 88: It gets worse as objects get smaller relative to resolution
Chart: 30 mm FOV
| 2.5340136054421768E-3 | 1.060657596371882E-2 | 1.8990929705215421E-2 | 6.422902494331066E-3 | 4.4501133786848069E-3 | 1.9518140589569164E-2 | 4.2687074829931967E-3 | 7.0861678004535147E-4 | 7.8854875283446701E-3 | 4.4841269841269845E-3 | 2.8571428571428567E-3 | 2.1882086167800455E-3
Thresh 1 | 0.075416 | 0.097084 | 0.39909 | 0.27709 | 0.090022 | 0.16164 | -0.087094 | -1 | 0.23029 | -0.25857 | -0.45634 | -0.10334
Thresh 2 | -0.042878 | 0.027711 | 0.31012 | 0.16678 | 0.034908 | 0.033188 | -0.15093 | -1 | 0.15081 | -0.36797 | -0.57079 | -0.19051

## Slide 89: What’s in a voxel?
Partial Volume Effect
  Grayscale/CT number reflects attenuation within voxel
  Voxels with multiple materials will have some averaged CT number
Blurring
  Contamination from, and transfer to, surrounding voxels
Operating assumption: attenuation conserved

## Slide 90: Reminder: PSF on thin features
“Real”
aperture
Measured
profile
1/2D Example: Fracture aperture

## Slide 91: 3D PSF effect on spheres (midsection)
As object gets smaller compared to rPSF, object gets dimmer, and “correct” threshold falls
rPSF = 2-sigma diameter of Gaussian smoothing curve, or 4s radius
Ketcham and Mote, 2019

## Slide 92: Segment by including the blurring
Idea: Capture the entire volume that includes the signal from the grain
Start with a generous
threshold…
and expand a bit from there

## Slide 93: Sum to get volume (again)
Numbers you need:
CTmat = CT number of matrix
CTf = “True” CT number of feature
2D example of 3D operation

## Slide 94: “PVB” method can get good answer at all sizes…
Chart: 30 mm FOV
| 2.5340136054421768E-3 | 1.060657596371882E-2 | 1.8990929705215421E-2 | 6.422902494331066E-3 | 4.4501133786848069E-3 | 1.9518140589569164E-2 | 4.2687074829931967E-3 | 7.0861678004535147E-4 | 7.8854875283446701E-3 | 4.4841269841269845E-3 | 2.8571428571428567E-3 | 2.1882086167800455E-3
Thresh 1 | 0.075416 | 0.097084 | 0.39909 | 0.27709 | 0.090022 | 0.16164 | -0.087094 | -1 | 0.23029 | -0.25857 | -0.45634 | -0.10334
Thresh 2 | -0.042878 | 0.027711 | 0.31012 | 0.16678 | 0.034908 | 0.033188 | -0.15093 | -1 | 0.15081 | -0.36797 | -0.57079 | -0.19051

## Slide 95: “PVB” method can get good answer at all sizes…
Chart: 30 mm FOV
| 2.5340136054421768E-3 | 1.060657596371882E-2 | 1.8990929705215421E-2 | 6.422902494331066E-3 | 4.4501133786848069E-3 | 1.9518140589569164E-2 | 4.2687074829931967E-3 | 7.0861678004535147E-4 | 7.8854875283446701E-3 | 4.4841269841269845E-3 | 2.8571428571428567E-3 | 2.1882086167800455E-3
Thresh 1 | 0.075416 | 0.097084 | 0.39909 | 0.27709 | 0.090022 | 0.16164 | -0.087094 | -1 | 0.23029 | -0.25857 | -0.45634 | -0.10334
Thresh 2 | -0.042878 | 0.027711 | 0.31012 | 0.16678 | 0.034908 | 0.033188 | -0.15093 | -1 | 0.15081 | -0.36797 | -0.57079 | -0.19051
PVB | 0.061821 | -0.13429 | -0.085869 | 0.073342 | 0.020331 | -0.011535 | -0.062438 | -0.049306 | 0.032255 | 0.0030581 | 0.032448 | 0.068175

## Slide 96: … and scales and instruments!
Chart: Grain
| 1.05 | 2.0499999999999998 | 3.05 | 4.05 | 5.05 | 6.05 | 7.05 | 8.0500000000000007 | 9.0500000000000007 | 10.050000000000001 | 11.05 | 12.05
Estimated | 0.019507 | 0.01898 | 0.010601 | 0.0064193 | 0.0044816 | 0.007881 | 0.002187 | 0.0025326 | 0.0028555 | 0.0042663 | 0.0044476 | 0.00070822
ACTIS scan | 0.017477 | 0.016291 | 0.0097515 | 0.0066092 | 0.0044365 | 0.0079674 | 0.0024415 | 0.0026732 | 0.0031137 | 0.0042781 | 0.0044501 | 0.00072581 | 0.017896 | 0.016867 | 0.0093014 | 0.0066311 | 0.0042574 | 0.0079281 | 0.002466 | 0.0026079 | 0.0029191 | 0.0041496 | 0.0044502 | 0.00072728 | 0.018673 | 0.016619 | 0.0094452 | 0.0068375 | 0.0046844 | 0.0082323 | 0.0024346 | 0.0027341 | 0.0031486 | 0.0040845 | 0.0044501 | 0.00070896 | 0.018808 | 0.016823 | 0.0089825 | 0.0067569 | 0.0044762 | 0.0079957 | 0.0023145 | 0.0026729 | 0.0029475 | 0.0038968 | 0.0044501 | 0.00069051 | 0.020911 | 0.017014 | 0.0096715 | 0.0070809 | 0.0050882 | 0.0090752 | 0.0024361 | 0.0028683 | 0.0031136 | 0.0038258 | 0.0044501 | 0.00053862
Within each subset, resolution decreases from left to right
Volume < 6 voxels

## Slide 97: Threshold for correct volume varies with size and shape
Chart: Radius (Equivalent Sphere) / Radius (PSF)
| 2.9689715803264525 | 2.9002103543779527 | 2.4442220194194042 | 2.1470014072052268 | 1.8798726962467902 | 2.2850108966671883 | 1.5405261894487785 | 1.5877971771026573 | 1.6706067907885105 | 1.8572308282564991 | 1.8817930673636623 | 1.0281531985023666
auw | 0.37995 | 0.40309 | 0.41896 | 0.40262 | 0.37196 | 0.37965 | 0.38256 | 0.3622 | 0.34238 | 0.37632 | 0.39002 | 0.33978
auwA | 0.33405 | 0.37917 | 0.38639 | 0.36392 | 0.2999 | 0.35497 | 0.39747 | 0.36313 | 0.35787 | 0.33233 | 0.31535 | 0.34684
auwB | 0.30549 | 0.3499 | 0.3257 | 0.33095 | 0.27268 | 0.31064 | 0.29328 | 0.2837 | 0.26231 | 0.30215 | 0.31425 | 0.24435
auwC | 0.24341 | 0.29296 | 0.2647 | 0.2533 | 0.20606 | 0.25138 | 0.2132 | 0.2326 | 0.19025 | 0.22789 | 0.24099 | 0.15075
auwD | 0.20556 | 0.22855 | 0.21843 | 0.19256 | 0.15621 | 0.19491 | 0.15658 | 0.16095 | 0.13803 | 0.17711 | 0.17148 | 0.081304
goldBL | 0.42044 | 0.44575 | 0.42477 | 0.41672 | 0.38289 | 0.39247 | 0.38897 | 0.37813 | 0.35984 | 0.40089 | 0.3991 | 0.35472
goldFqtz | 0.30412 | 0.33493 | 0.31565 | 0.32067 | 0.27658 | 0.29858 | 0.28536 | 0.28503 | 0.2482 | 0.29504 | 0.29879 | 0.21825
goldFgrt | 0.29898 | 0.32099 | 0.31723 | 0.30795 | 0.25774 | 0.28745 | 0.27569 | 0.27597 | 0.24204 | 0.28106 | 0.27767 | 0.22797
goldBLlr | 0.28493 | 0.31671 | 0.29735 | 0.29149 | 0.23178 | 0.27074 | 0.25226 | 0.25331 | 0.2142 | 0.25985 | 0.24621 | 0.16137
Sphere | 0.027 | 0.13317 | 0.23615 | 0.30288 | 0.3681 | 0.40112 | 0.42112 | 0.45075 | 0.46687 | 0.47555 | 0.48042
Cube | 0.047614 | 0.18344 | 0.28084 | 0.33108 | 0.3883 | 0.41945 | 0.44066 | 0.44987 | 0.45244 | 0.45339 | 0.45395
Dome | 0.4912 | 0.45938 | 0.39156 | 0.32402 | 0.23744 | 0.18519 | 0.15176 | 0.10364 | 0.076661
Two scanners, same trend when normalized by measured PSF
Main shape concerns: surface to volume ratio; corners

## Slide 98: Shape affected a bit…
High-res
Low-res
The trick: Customize each threshold based on PVB-corrected volume

## Slide 99: Shape and orientation recoverable, but affected by blurring
Shape stable (consistent across resolutions) if 3rd axis > rPSF
Orientation of 1st or 3rd axis stable if varies from intermediate by > ×2

## Slide 100: Details to consider
Calibration
  How do you get CTmat?
  How do you get CTf?

## Slide 101: CTmat is easy
Just measure an average value for matrix
If heterogeneous or locally variable, you can measure only matrix surrounding feature
  Encompass boundary blurred into grain; rPSF

## Slide 102: Ways to get CTf
Brightest parts of largest grains?
  Possible, if shortest dimension > 2rPSF
Calibrate using a “known” grain
  Phantom would need same size, shape, composition as sample
  Best: higher-res subvolume scan to image grain at sufficient resolution
    Resolution invariance: if you get one right, you get the rest right
First principles?
  Calculate expected CT number, based on composition…

## Slide 103: Can CTf be derived from first principles?
Chart: X-ray energy (keV)
Chart: 150 kV spectrum
Chart: 80 kV spectrum

## Slide 104: CTf depends on X-ray spectrum AND particle composition AND size AND what’s surrounding it (AND…)
Chart: Modeled (curves) versus measured (points) attenuation contrast
| 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
80 kV qtz | 139.4557 | 143.4082 | 145.8489 | 147.335 | 148.1909 | 148.6175 | 148.7447 | 148.66 | 148.4235
80 kV grt | 139.4557 | 148.7719 | 145.6917 | 141.7097 | 138.0765 | 134.928 | 132.2177 | 129.8755 | 127.8378
150 kV qtz | 147.6704 | 151.8624 | 154.8022 | 156.9677 | 158.6325 | 159.9628 | 161.0645 | 162.0073 | 162.8382
150 kV grt | 147.6704 | 161.9035 | 166.3622 | 170.0596 | 173.6733 | 177.0692 | 180.0443 | 182.4588 | 184.2531

## Slide 105: CTf depends on X-ray spectrum AND particle composition AND size AND what’s surrounding it (AND…)
Some trends match expectation: grt increases CTf at 150 kV, decreases at 80 kV
Chart: Modeled (curves) versus measured (points) attenuation contrast
| 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
80 kV qtz | 139.4557 | 143.4082 | 145.8489 | 147.335 | 148.1909 | 148.6175 | 148.7447 | 148.66 | 148.4235
80 kV grt | 139.4557 | 148.7719 | 145.6917 | 141.7097 | 138.0765 | 134.928 | 132.2177 | 129.8755 | 127.8378
150 kV qtz | 147.6704 | 151.8624 | 154.8022 | 156.9677 | 158.6325 | 159.9628 | 161.0645 | 162.0073 | 162.8382
150 kV grt | 147.6704 | 161.9035 | 166.3622 | 170.0596 | 173.6733 | 177.0692 | 180.0443 | 182.4588 | 184.2531
80 kV qtz | 148.7492 | 108.6693
80 kV grt | 92.184
150 kV qtz | 142.1375 | 117.5403
150 kV grt | 119.4
But why the dropoff?

## Slide 106: CTf depends on X-ray spectrum AND particle composition AND size AND what’s surrounding it (AND…)
And beam-hardening correction throws another spanner in the works…
Chart: Modeled (curves) versus measured (points) attenuation contrast
| 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
80 kV qtz | 139.4557 | 143.4082 | 145.8489 | 147.335 | 148.1909 | 148.6175 | 148.7447 | 148.66 | 148.4235
80 kV grt | 139.4557 | 148.7719 | 145.6917 | 141.7097 | 138.0765 | 134.928 | 132.2177 | 129.8755 | 127.8378
150 kV qtz | 147.6704 | 151.8624 | 154.8022 | 156.9677 | 158.6325 | 159.9628 | 161.0645 | 162.0073 | 162.8382
150 kV grt | 147.6704 | 161.9035 | 166.3622 | 170.0596 | 173.6733 | 177.0692 | 180.0443 | 182.4588 | 184.2531
80 kV qtz | 148.7492 | 108.6693
80 kV grt | 92.184
150 kV qtz | 142.1375 | 117.5403
150 kV grt | 119.4
150 kV qtz (no BHC) | 111.5
150 kV grt (no BHC) | 107.1

## Slide 107: Takeaways
“Seeing” is one thing, measuring is another
  When feature is small relative to data resolution, special care is needed
  Global thresholds don’t work
  Guessing is… guessing

## Slide 108: More examples
Steel
Tungsten
Chart: Threshold volume (mm3)
Tungsten and steel shot into particle board
Distinguish multiple phases by plotting size vs. max or mean CT number
Plotting vs. maximum (or mean) CT number is a useful trick…
But keep possible shape effects in mind
Deblurring
With beam hardening?

## Slide 109: Distinguishing multiple phases
25 mm
garnet
ilmenite mixed with quartz and feldspar
garnet
zircon

## Slide 110
Chart: threshold-determined volume (mm³)
Distinguishing multiple phases

## Slide 111
Chart: threshold-determined volume (mm³)
Distinguishing multiple phases

## Slide 112
Chart: threshold-determined volume (mm³)
zircon
garnet
ilm+
qtz+spar
Distinguishing multiple phases

## Slide 113: So, what’s in a CT number?
PVB approach works on any small feature
  Grains, pores, etc.
  Volumes are accurate, resolution-invariant
  Shape and orientation dicier, but we can tell when they become unreliable
“Attenuation conservation” principle works
  But, there are devils in the details
  Calibration needs to be empirical at this point

## Slide 114
End of Part 3

## Slide 115: Moving on to the Continuum
Pore space often shows up well in CT
  Big density difference between rock and void!
  If pores are too small to be resolved individually, they can still be detected

## Slide 116: Partial porosity measurement
25-mm mini-cores
“Align3D”
(or other tools)

## Slide 117: Incipient alteration
3R
11R

## Slide 118: High alteration
9R
17R

## Slide 119: Recent results from Chicxulub
Pre-flow test
After drying(!!)
Difference
Standard drying step for permeability analysis (40°C oven)
dessicated clay particles!

## Slide 120: It’s a gas!
from Hanna et al, 2022
Porosity in matrix and fine-grained rims in Murchison meteorite
Xe gas at 2.76 MPa (400 psi; 27.2 atm)

## Slide 121
End of Part 3