## Slide 1: Overview of UTCT and XCT in Planetary Sciences
Romy Hanna
UTCT
Jackson School of Geosciences
University of Texas at Austin

## Slide 2: Part I: An Introduction to UTCT
Notes: So, part one, an introduction to our lab.

## Slide 3: UTCT Lab and its History
1997: First instrument acquisition
1999: Became NSF-supported multi-user facility
  Renewed 2001, 2004, 2007, 2010, 2013, 2016, 2018, 2022, 2025 RCE
2023: Became NASA Planetary Science Enabling Facility (PSEF)
Notes: We acquired our first instrument in 1997

## Slide 4: What We Do
Research
Software Development
Short Courses
High porosity areas around CM Murchison chondrule (Hanna et al. 2022)
Quant3D
XCT Imaging

## Slide 5: Zeiss 620 XRM
DCT: Barred olivine orientations
30-160 kV source up to 25 W
Imaging objects ranging from ~14 cm across to < 1 mm
Feature detectability to 0.5 µm and voxel size to ~0.04 µm (depending on sample size)
X-ray diffraction contrast tomography (DCT): 3D crystallographic orientations in sufﬁciently small samples (< 2 mm)

## Slide 6: NSI Scanner
450 kV source for large (~dm-scale) or highly-attenuating objects
225 kV source with 5-µm spot size for detailed imaging of most samples
Helical scanning for objects with high aspect ratios such as cores
'SubpiX' mode for creates a virtual detector with ~2X higher spatial resolution than traditional scanning
Apollo Drive Tube 73002 with SubpiX imaging
Emerald-bearing rock imaged with 450 kV source

## Slide 7: Wide Variety of Clients and Projects
In last 3 years alone, 209 PI-led projects for over 8,000 hours of scanning
Clients and applications span many disciplines
Metapelite; Nagurney et al., 2022
Deep-sea foraminifera; Belanger 2022
Dust in filter media; Song and Shim 2022
Notes: In the following slides I highlight some research led by UTCT-supported PIs that has significantly contributed to research
These three recent figures show the breadth from biology, to engineering, to geology on the right, all using data produced by our lab.
Nagurney – garnet P/T conditions for crystallization by analyzing their 3D distribution and CSD

## Slide 8: Paleontology
Descriptive and quantitative morphology
Curatorial
  Library of Digital Morphology http://www.digimorph.org
  Contributions to MorphoSource.org (biological specimens)
Inner ear morphological analysis of lizards; Latimer et al. 2023
Digitally isolated skull bones of a fossil reptile Abel et al. 2022
Notes: - In paleontology CT is now used for the majority of descriptive and quantitative morphology research.
It also has a large Curatorial aspect.
Our lab developed the Digimorph Digital Morphology library that is widely used to examine the 3D structure of fossilzed and recent vertebrates, and we have also recently begun a collaboration with Morphosource, which is it’s biological counterpart, run out of Duke University.

## Slide 9: 3D Petrography
2D: Like having 1000s thin sections, in all orientations
3D: Volume rendering
Hunting for tiny stuff like gold grains
Ferraz de Costa et al., 2022
Notes: - When it comes to classical geology, CT essentially provides a way to do 3D petrography.
-Trying to find gold grains in an ore via thin sectioning is painful, but with xCT one can quickly find these highly attenuating grains in the volume and measure their abundance as well as investigate their distribution and 3D relationship to other phases. Purple – sulfide, blue arsenopyrite, yellow gold

## Slide 10: Structural Geology
Can find “asymmetry flip” orientation for each porphyroblast in volume using the inclusion trails
Huddlestone-Holmes and Ketcham (2010)
Notes: XCT has also done a lot for structural geology research
Specifically, the inclusion fabric orientations within the garnets can be used to rescontruct the local strain orientation during their formation.
- The application of XCT to this problem was pioneered by a student from our lab.

## Slide 11: “Look before you dissolve”
Mounting and screening magnetite for (U-Th)/He work (Emily Cooperdock; former UTCT PhD student)
Notes: - This last example is more recent work we’ve been doing integrating geochronology and XCT.
- These images show a new process developed by a previous student Emily Cooperdock, for screening magnetites prior to Uranium thorium He dating.

## Slide 12: “Look before you dissolve”
1 mm
1 mm
Is it magnetite just because a magnet grabs it?
Cooperdock and Stockli, 2016
Notes: She found that screening individual magnetites prior to dissolution was key, as many seemingly magnetite particles picked out using the traditional technique of a magnet where not pure magnetite and thus not suitable for combining to derive a single thermochron date.

## Slide 13: CT and geo/thermochronology
2D measurement
CT Scan
Apatite
Find inclusions; measure precise volume, FT; shape analysis – Rich Ketcham new work
1 mm
Notes: Our director Rich ketcham is also heavily involved in geo/thermocronology is extending Blob3D to do shape analysis using spherical harmonics on detrial zircons.

## Slide 14: Object Measurement with Blob3D
Segmentation of object (phase/mineral/void) voxels
Separation of touching objects
Measurement of objects, including shape and orientation analyses

## Slide 15: Mineral Fabrics with Quant3D
Foliated Rhyolite
Henry Mountains, Utah
SVD, 3D Rose Diagram
Amphibole Orientations
Amphibole
Oxide
5 mm
Sample courtesy of E. Horsman, University of Wisconsin

## Slide 16: MuCalc Worksheet

## Slide 17: Part II: XCT in the Planetary Sciences
A tour of what is possible with XCT!

## Slide 18: Nakhlite Fracture Networks
Needham et al. (2013)
3D fracture network from XCT and 2D thin section analyses allowed mapping of alteration pathways

## Slide 19: Chondrule Deformation
CM Murchison chondrules
Hanna et al. (2015)
Hand-drawn orthogonal planes
Orientated thin section
Chondrules foliated from impact

## Slide 20: Micrometeorite Entry Dynamics
3D porosity profiles (temperature proxy) and shape analysis demonstrate spinning atmospheric flight entry of MMs
Dionnet et al. (2020)

## Slide 21: Nebular Accretion Models
From Hanna and Ketcham (2018)
Rim volume – chondrule size / rim volume relationship supports nebular formation model for dust rims in meteorite CM Murchison.

## Slide 22: Curation
Apollo drive tubes (ANGSA)
73002
Eckley et al. 2025
Bennu particles
(OSIRIS-REx)
Eckley et al. 2025

## Slide 23: Impact Melt Cooling History
2 cm
From Benedix et al. (2008)
and Hanna and Ketcham (2017)
Impact melt sheet cooled on asteroid
Metal-sulfide contacts record gravitational field
Vesicles elongated due to flow
L Chondrite
PAT 91501

## Slide 24: Silicate Partial Melting
H7 Watson 012
Plagioclase 3D grain connections showing melt network in grain-supported matrix – slow cooling at depth.
Tait et al. (2014)

## Slide 25: CI Chondrite “Sediments”
Segmented clasts show weak lineation consistent with linear alignment during shear-dominated movement (impact? Seismic shaking?)
Friedrich et al. (2025)
CI Ivuna

## Slide 26: Planetary XCT Data Repositories and Archival